## Slide 1: APPLICATIONS of HIGH ENERGY PHYSICS –( R&D, IDEAS, TECH )– .: mainly particle accelerators and detectors :.
R. Mountain
Syracuse University

## Slide 2: Overview
Applications of High Energy Physics
  Particle physics is a basic science (no direct applications), but…
  There is a great deal of:
    R&D (needed to build accelerators and detectors for HEP),
    Ideas and concepts generated (incl. theoretical), and
    Practical technological developments
  Will consider these as applied to other fields and disciplines
  Beyond the technology, what is unique to particle physics is the scale of the science: its size and complexity. Dealing with scale issues is also exportable to other fields
Near Fields — (other) physics, astronomy, geology, …
Far Fields — medicine, electronics, computing, …
Really Far Fields — energy, defense, industry, …
Take a random walk through some of these other fields…

## Slide 3: No Higgs Today!

## Slide 4: APPLICATIONS IN CONDENSED MATTER physics
Part I.
  Material Structure

## Slide 5: Material Structure with SLS
Origin
  Synchrotron radiation: GE, 1946
  SLS: ~1980s
Technique
  Use synchrotron light source (SLS = dedicated accelerator)
  Crystallography: X-ray diffraction technique
Physics
  Interference pattern made by transmission or reflection of x-rays from a crystal (Bragg scattering)
  Also by x-ray fluorescence (like scintillator but excitation by x-rays)
  Examine diffraction pattern
  Reconstruct crystal structure: atomic locations, electron orbital densities, etc.
  Computationally model crystal structure of material

## Slide 6: Crystallographic Patterns
X-ray diffraction pattern, single aluminum crystal,
H.J. Milledge, University College, London
X-ray diffraction patterns,
nano-crystal lattices,
www.chess.cornell.edu
DNA structure, 1950s

## Slide 7: Crystallographic Patterns
protein crystallography:
RNA polymerase,
30,000 individual atoms

## Slide 8: Synchrotron Light Sources
Accelerator Facilities
  Dozen facilities worldwide
    NSLS Brookhaven, SSRL Stanford, ALS Berkeley, APS Argonne, CHESS Cornell …
  Multi-disciplinary research
    physics, chemistry, biology, materials science, environmental science, art
  Using HEP accelerator tech to study structure and function
Synchrotron Radiation
  Photons generated by acceleration of e–,p beam (bend, wiggler magnets)
    do this on purpose!
  Broad energy spectrum (tunable)
  High intensity on target
SOLEIL, France
NSLS, BNL
wigglers
bending

## Slide 9: MEDICAL APPLICATIONS
Part II.
  Medical Imaging
  Clinical Treatments (e.g. Oncological)

## Slide 10: X-Rays
Origins
  Wilhelm Conrad Roentgen, 1895
  First Nobel Prize, 1901 (detector)
Technique
  Imaging: use x-rays to shadow object, create latent image on photographic film, or energy pattern on CCD camera
  Therapeutic: use x-ray beam to deposit energy in object (e.g. cancer cells)
Physics
  X-rays penetrate object, pass through with some amount of attenuation (either small or large, depends on Z)
    Small: passes through, transmitted, can be used to create an image (imaging)
    Large: deposits energy, locally heats object (therapeutic, “conventional” radiotherapy)
  Behavior is similar for all photons (X, Gamma, UV, VIS, …)
Advantages
  Relatively simple
  Depends on Z
Roentgen’s wife
(first x-ray image)
Modern x-ray
image

## Slide 11: Positron Emission Tomography (PET)
Origins
  1960s
Technique
  Imaging device, 2D or 3D
  Use radionuclide tracer technique (tracer = biochemical agent which bonds with target cancer cells, e.g. 18F-FDG)
Physics
  Radionuclide decays, emitting +
  + annihilates with e– from tissue, forms back-to-back 0.511 MeV gamma pair
  Gamma pairs are detected using PMT + crystal scintillators in a ring arrangement
Analysis
  Make time coincidence (∆t < 6–12 ns) between any pair of these detectors
  Each detector pair defines a line
  Reconstruct position of radiotracer by intersection of all such lines
  Can add TOF (time-of-flight) info to reduce noise, correct ions for attenuation, scattering, noise, etc.
Davis Meltzer, National Geographic
Positron travels short distance in tissue
Positron Annihilation
From J. Karp, Positron Emission Tomography, Fermilab colloquium, 2004
in tracer

## Slide 12: PET Images
(FDG)

## Slide 13: Proton Therapy (PT)
Origin
  Developed by: Robert Wilson, Harvard, 1946
  Purpose: Cancer treatment
Technique
  Cyclotron (accelerator)
  Accelerate protons to low energies, KE≈200 MeV
  Shoot proton beam at patient: head, body, extremity
Physics
  Protons penetrate the body, deposit energy along path, until it has lost enough and then stops in the body
  Bragg curve: deposits most of energy at end of its path, called “ranging out”
  Calculate energy needed for proton to reach target tumor (range) and it will deposit most of its energy into the tumor only, and only a small amount into intermediate tissue
Clinical
  Operation: energy heats cancer cells
    impeding cell division, plus
    damaging cells, increasing probability of cell death
Advantages
  Differs from conventional (x-ray) radiation therapy:
    Proton is a “depth charge” as used in PT
    Gamma-rays are like a penetrating laser, damaging tissue on straight line, before/after/in tumor
Facilities: 12 in USA, ~6 online soon

## Slide 14: NPTC @ MGH — Cyclotron
Northeast Proton Therapy Facility @ Mass General Hospital, Boston MA
Louvain #00

## Slide 15: NPTC @ MGH — Beamline
Extraction Line
Beam Line

## Slide 16: NPTC @ MGH — Patient Area
Patient
Arm
(rotates)
230 MeV protons
Aperture
Gantry

## Slide 17: Heidelberg Therapy Facility
acceleratorsamerica.org

## Slide 18: Gamma Knife
Origins
  L. Leksell, Stockholm, 1951
  Cyberknife, 1994 (feedback)
Technique
  Uses intense radioactive sources: 60Co gamma-rays
  Purpose: non-invasive treatment of brain tumors
Physics
  Collimating of gamma-rays into many precision beams
  Relies on intensity superposition of gamma-ray beams
Clinical
  Similar to conventional radiation therapy, with same drawbacks
  Facilitates treatment of small targets deep within the brain
Upstate Gamma Knife Center

## Slide 19: Applications to archaeology
Part III.
  Muon Tomography

## Slide 20: Muon Tomography
Origin
  Luis Alvarez, 1968
  Imaged Khefe Pyramid (2nd Giza), in search of… hidden chambers
Technique
  Uses cosmic rays
  Uses directional detectors in a large array
Physics
  Passing muons are preferentially absorbed by denser material
  Scattering dominates resolution
  Map flux in a given direction
  Reconstruction of density in 3D using standard computational tomography
From: Schwitters, Imaging Maya Pyramids with Cosmic Ray Muons, 2008

## Slide 21: Security / defense applications
Part IV.
  MST
  Backscatter

## Slide 22: Muon Scatter Tomography
Technique
  Similar to muon tomography but uses scattered muons instead of straight-throughs
  Use tracking detectors like drift chambers, to get direction of muon
  Non-invasive
Physics
  Coulomb (EM) scattering
  Scattering goes like density: denser, high-Z materials scatter more
  Use timing to see muons that scatter and reconstruct to the scattering point
Applications
  Large size objects
  Cargo containers , trucks, etc.
  Hidden nukes under layers of steel

## Slide 23: Backscatter Scanners
Origin
  Towe & Jacobs, 1981
  9/11
Technique
  Uses x-rays
  Point-source or scanning beam source
Physics
  Compton scattering, select large angles
  Energy tuned to penetrate clothing, not skin
  Dose: equivalent to 2 min high altitude flight (TSA)
Applications
  Airport security
  Cargo containers, trucks
  One side only needed to scan
TRANSMISSION
BACKSCATTER

## Slide 24: Backscatter vs Transmission

## Slide 25: Backscatter Images
Susan Hallowell, Director of TSA’s research lab, c.2011.
Backscattered x-rays are light, while absorbed x-rays are dark
Backscatter scanners: two, for front and back images
(also in airports are millimeter wave scanners, which uses EHF RF frequency waves)

## Slide 26: Mobile Backscatter Van
New twist
  Package backscatter scanner into a van: ZBVTM
  Mobile unit
    (not Google Street View)
  Still delivers dose

## Slide 27: Applications TO ELECTRONICS AND COMPUTING
Part V.
  Radiation Damage
  Computing Techniques

## Slide 28: Radiation Damage to Micro-Electronics
Background
  Cosmic ray radiation exists and can damage electronics when passing through silicon
  Damage can be serious and can affect operation of:
    Satellites … who cares?
    Spacecraft … meh?
    Airplanes … what?
    iPhones … NO!
  Enhanced radiation environment at high altitudes is similar to HEP accelerator environment
  Effects have small probability, and so depend on the dose rates
Effects
  Damage usually to digital electronics, so effects are seen in damage to computers
    esp. bit flips in memories, called single-event upsets (SEU)
    many other effects
  Micro-Electronics (chips) can be rad-hard or rad-soft
  Need to measure tolerances for rad damage for various components and develop mitigation strategies to avoid big problems
  Have measured this ourselves and seen these effects (and others)
0
1
1
0
4-bit word
= 6
1
1
0
1
= 14
cosmic ray
flips a bit…
MEMORY

## Slide 29: Typical Test Setup (SU HEP)
Aperture
Ø12.7 mm
Ion Chamber
FPGA Board
p Beam
Adjustable
mechanics

## Slide 30: Computing & Networks
World Wide Web
  WWW invented at CERN ***
  Invented to solve the problem of communicating in an international collaboration of thousands of physicists (for the LHC generation)
  Not Internet (DARPA)
Massive data handling
  Hardware farms, algorithms for parallel computing
  Cloud / Grid computing
Simulation and Analysis Tools
  GEANT, EGS, FLUKA large HEP simulation software packages applied to other fields
  ROOT interactive statistical analysis tool
Programming and Algorithmic Advances
  Neural nets
  Decision trees
  Principal component analyses
  etc. etc. …

## Slide 31: Had Enough?

## Slide 32: The Future: Are We There Yet?
How will High Energy Physics impact the Future?
Ours is a basic science…
– Faraday, 1840s
– Rutherford, 1911
– Higgs, 2012
What is the use of a small child ?